## Slide 1: A Reconfigurable FTL (Flash Translation Layer) Architecture for NAND Flash-Based Applications
2021. 03. 24
Presentation by Lee, Sounghyoun
leesh812@dankook.ac.kr
C. Park et al.

## Slide 2
Introduction
Background
Related Work
Flexible Group Mapping
Performance Model and Analysis
Conclusion

## Slide 3: 1. Introduction
Google Finance
NAND Flash memory become more common in many mobile devices
  It is nonvolatile, reliable, more resistant to physical shocks and uses less power
  NAND flash memory is characterized by its erase-before-write operation
    This necessitates FTL(Flash Translation Layer)
  ex) MP3 players, MMC cards, cellular phones, and PDAs

## Slide 4: 1. Introduction
Google Finance
NAND Flash memory become more common in many mobile devices
  It is nonvolatile, reliable, more resistant to physical shocks and uses less power
  NAND flash memory is characterized by its erase-before-write operation
    This necessitates FTL(Flash Translation Layer)
  ex) MP3 players, MMC cards, cellular phones, and PDAs

## Slide 5: 1. Introduction
Google Finance
Important Factors that affects FTL design
  Hiding the technological detail
  Maximizing the performance and lifetime
  Access patterns of applications

## Slide 6: 2. Background
Google Finance
  Page-write requests
    four page-read operations
    four page program operations
    two block-erase operations
  Reducing the numbers of merge operations

## Slide 7: 3. Related Work
Google Finance
Page Mapping
  LPN : Logical Page Number
  PPN : Physical Page Number
An efficient “garbage collection”
It requires a very large amount of memory space for the map table

## Slide 8: 3. Related Work
Google Finance
Block Mapping
  LBN : Logical Block Number
  PBN : Physical Block Number
Considerable performance degradation over random-access patterns

## Slide 9: 3. Related Work
Google Finance
Hybrid Mapping
  Compromises between page mapping and block mapping
    many hybrid mapping schemes reduce the mapping table size and the block copy overhead

## Slide 10: 4. Flexible Group Mapping
Google Finance
Flexible Group Mapping
  Based on the log block scheme
  Configures the degree of sharing of log blocks among data blocks
  Manages the degree of the allocation of log blocks for the frequently updated data blocks

## Slide 11: 4. Flexible Group Mapping
Google Finance
Flexible Group Mapping – Write Scheme
  DBMT : the data-block-mapping table
  LBMT : the log-block-mapping table
  LPMT : the log-page-mapping table
  DGN : the data-block-group number

## Slide 12: 4. Flexible Group Mapping
Google Finance
Flexible Group Mapping – Merge Scheme
  Simple merge operation
  Swap merge operation
  Copy merge operation

## Slide 13: 4. Flexible Group Mapping
Google Finance
Flexible Group Mapping – Merge Scheme
  Simple merge operation
  Swap merge operation
  Copy merge operation

## Slide 14: 4. Flexible Group Mapping
Google Finance
Flexible Group Mapping – Merge Scheme
  Simple merge operation
  Swap merge operation
  Copy merge operation

## Slide 15: 5. Performance Model and Analysis
Google Finance
Workload Analysis
  denotes the th write request
  The request density

## Slide 16: 5. Performance Model and Analysis
Google Finance
Workload Analysis

## Slide 17: 5. Performance Model and Analysis
Google Finance
Performance Analysis
  : the active data block accessed by
  : the active data block group accessed by
  and : the set of active blocks and the set of active block groups
  : the number of log blocks associated with
Memory Requirement Analysis

## Slide 18: 6. Experimental Results
Google Finance
Experiment

## Slide 19: 6. Experimental Results
Google Finance
Experiment

## Slide 20: 6. Conclusion
Google Finance
Conclusion
The proposed reconfigurable FTL architecture efficiently handles diverse NAND flash applications ranging from MP3 to SSD for a PC
In order to efficiently explore the design space, a workload analysis method based on the density distribution of given requests and the update frequency is proposed
The experimental results show
  the proposed architecture can be reconfigured to a given workload ranging from MP3 to PC applications
  the proposed analysis method can efficiently find the optimal N and K values within a reasonable amount of time

## Slide 21: A Reconfigurable FTL (Flash Translation Layer) Architecture for NAND Flash-Based Applications
2021. 03. 24
Presentation by Lee, Sounghyoun
leesh812@dankook.ac.kr
Thank you!
C. Park et al.