## Slide 1: Application-Managed Flash
2021. 06. 02
Presentation by Han, Yejin
hyj0225@dankook.ac.kr
Sungjin Lee, Ming Liu, Sangwoo Jun, and Shuotao Xu, Jihong Kim, Arvind
14th USENIX Conference on File and Storage Technologies (FAST ‘16). 2016.

## Slide 2
Introduction
Motivation
AMF
3-1. Block I/O interface
3-2. ALFS
3-3. AFTL
4. Evaluation
5. Conclusion

## Slide 3: 1. Introduction
  NAND flash SSD become the preferred storage device in consumer electronics and data centers
  FTL provide an block I/O abstraction for interoperability with HDDs
File System
Read Sectors
Write Sectors
Read Sectors
Write Sectors
File System
Block Device Interface
Block
Read /Write Erase
Pages
Device Driver
Flash Memory
FTL
Device Driver
Flash Memory
Read Sectors
Write Sectors

## Slide 4: 2. Background
What are the purposes of the FTL?
Require significant hardware resources
Extra I/Os for flash management (GC)
Host applications cannot predict the
bahavior of flash storage
Z
  Managing address translation, Garbage collection, wear-leveling, …

## Slide 5: 2. Background
What are more issues of the FTL?
  Double logging between the FTL and the Host (double logging)
  Wastes hardware resource and increases write pressure to flash devices
Z
Duplicate Functionality

## Slide 6: 3. AMF
Device-managed Flash
Application-managed Flash
moves flash management
from the device to applications

## Slide 7: 3. AMF
Block I/O interface
ALFS (AMF Log-structured File System)
AFTL (AMF Flash Translation Layer)
Application-Managed Flash

## Slide 8: 3. AMF
Block I/O Interface
  AMF I/O is based on conventional block I/O
0
1
2
3
4
5
6
7
8
9
4KB Sector
(IO: READ/WRITE)
Host
Device
Host Application
Channel #0
Channel #1
Channel #2
Channel #3
…
…
…
…
10 11 12 13 14 15 16 17 18 19 20 21 22 23 24 25 26 27 28 29 30 31
0
4
8
12
1
5
9
13
2
6
10
14
3
7
11
15
…
Physical
Segment 0
Logical Segment 0
(IO:TRIM)
Logical Segment 1
Appending

## Slide 9: 3. AMF
Block I/O Interface
  Append-only Write
Host
Device
Host Application
Logical Segment 0
Logical Segment 1
Appending new data (WRITE)
…

## Slide 10: 3. AMF
Block I/O Interface
  Only sequential writes with no in-place updates
  Sectors can be reused after the segment has been deallocated by TRIM
Host
Device
Host Application
Logical Segment 0
Logical Segment 1
Unable to overwrite
TRIM
Appending
…
Notes: 기존 OS는 NVM을 효과적으로 이용할 수 없다.

## Slide 11: 3. AMF
Block I/O interface
ALFS (AMF Log-structured File System)
AFTL (AMF Flash Translation Layer)
Application-Managed Flash

## Slide 12: 3. AMF
ALFS (AMF Log-structured File System)
AMF Block I/O Layer
Host
Device
AMF Log-structured File System (ALFS)
(based on F2FS)
AMF Flash Translation Layer (AFTL)
NAND Flash
Segment-level
Address Remapping
Wear-leveling &
Bad-block management
Notes: 기존 OS는 NVM을 효과적으로 이용할 수 없다.

## Slide 13: 3. AMF
ALFS (AMF Log-structured File System)
  File Layout and Operation
Notes: 기존 OS는 NVM을 효과적으로 이용할 수 없다.

## Slide 14: 3. AMF
ALFS (AMF Log-structured File System)
  Check-point segments for quick mount and recovery
  Inode-map segments for fast searches of inodes
Check-point segment handling
Managing inode-map block
Notes: Inode map size=2GB-> 4KB의 inode-map block으로 나눠서 관리
TIMB=2MB

## Slide 15: 3. AMF
ALFS (AMF Log-structured File System)
ALFS
with
AFTL
LFS
with
FTL
ALFS (AMF Log-structured File System)
  Comparison with conventional LFS
3 page copies + 2 block erasures
6 page copies + 3 block erasures
Notes: 기존 OS는 NVM을 효과적으로 이용할 수 없다.

## Slide 16: 3. AMF
Block I/O interface
ALFS (AMF Log-structured File System)
AFTL (AMF Flash Translation Layer)
Application-Managed Flash

## Slide 17: 3. AMF
AFTL (AMF flash Translation Layer)
Notes: 기존 OS는 NVM을 효과적으로 이용할 수 없다.

## Slide 18: 4. Evaluation
Data structures including TIMB need tiny amount of host DRAM
AFTL maintains a smaller mapping table than the page-level FTL

## Slide 19: 4. Evaluation
Performance measurment
EXT4: only the FTL performed GC
F2FS: both F2FS and the FTL performed GC
AMF: only ALFS performed GC
PFTL: no extra swapping I/Os
AFTL: no extra swapping I/Os
DFTL: incurred extra I/Os
Notes: Pftl-> tables in DRAM
aftl=->
Dftl-> in-flash mapping

## Slide 20: 4. Evaluation
For random writes,
AMF outperforms
all other schemes
For the heavy workload,
AMF achieves
the best performance

## Slide 21: 4. Evaluation
AMF outperforms
all other schemes
All five storage configurations show similar performance

## Slide 22: 4. Evaluation
AMF incurs 28% fewer erase operations overall compared to F2FS+DFTL

## Slide 23: 4. Evaluation
The CPU utilization of AMF
is similar to F2FS and EXT4
AMF has the shortest I/O
response times with small fluctuations

## Slide 24: 5. Conclusions
New block I/O interface exposing flash storage as append-only segments
Implementing new FTL scheme (AFTL) and a new file system (ALFS)
Reducing DRAM in the flash controller by 128X, impoving performance of the file system by 80%
https://github.com/chamdoo/bdbm_drv.git
https://github.com/sangwoojun/bluedbm.git
AMF

## Slide 25: Application-Managed Flash
2021. 06. 02
Presentation by Han, Yejin
hyj0225@dankook.ac.kr
Sungjin Lee, Ming Liu, Sangwoo Jun, and Shuotao Xu, Jihong Kim, Arvind
14th USENIX Conference on File and Storage Technologies (FAST ‘16). 2016.
Thank You!
Notes: Let me begin my presentation.
Today I will give a presentation on “Fully Automatic Stream Management for Multi-Streamed SSDs Using Program Contexts”