## Slide 1: Storage Abstractions for SSDs: The Past, Present, and Future
2024. 12. 17
Presentation by Yeojin Oh and Nakyeong Kim
oyj5420@dankook.ac.kr nkkim@dankook.ac.kr
X. Zhang., J. Bhimani., S. Pei., E.J. Lee., S.J. Lee., Y.J. Yoon., E.J. Kim., C.H. Choi., E.H. Nam., J.M. Choi., B.S. Kim. ATC’23 Syracuse University, Florida International University, Samsung Semiconductor Inc, Soongsil University, DGIST, FADU Inc, Dankook University

## Slide 2
Introduction
Background
  Block Layer
  Communication Protocol
  SSD
Abstraction Enhancement (4)
Future
Conclusion

## Slide 3: Introduction
Storage Abstraction
Modern computers use abstractions for interoperability between host and peripherals
SSD different from HDD
  Not mechanical device, but electrical
  Out-of-place updates (garbage collection necessity)
  Internal parallelism
  High internal bandwidth
SSD need new enhancement abstraction
  Not provide method to reduce GC overhead with host-SSD coord
  Data transfer between host and SSD pose limitation of utilization
  Tr. storage abstraction see storage in units of sectors
Host
Storage
1. Expose address range
2. Issue request
4. Return result
3. Execute operation
bottleneck

## Slide 4: Introduction
Categories
Extending block abstraction with host-SSD hints
  TRIM
  Multi-stream
  Flexible Data Placement
Enhancing host-level control over SSDs
  Open-channel SSD
  Zoned Namespaces SSD
Offloading host-level management to SSDs
  Key-value SSD
  Computational storage
Making SSDs byte-addressable
  Use in CXL

## Slide 5: Background
Block Layer
Most storage expose their capacity to OS and support 2 operations: read & write
Bio serve unifying interface between OS and various types of storage device
From first version(only two read/write tasks in 2001), many improvements were made by 2021
  To provide optional hint for improved I/O, introduced discard operation (TRIM)
  Added Multi-stream and Zoned Namespaces enhancements
  Allowed multi-queue design (blk-mq), scaling with # of host CPU cores
OS
Communication
SSD
v6.12.4 (latest)

## Slide 6: Background
Communication Protocols
Host and SSD must communicate in same language
SATA (Serial AT Attachment, 2001)
  Serve as high-speed serial link replacement for PATA of storage devices
  3 major versions: 1.0, 2.0 and 3.0 (improved transfer speed)
  SATA 3 is bounded with maximum transfer speed of 6GB/s
NVMe (NVM Express, 2011)
  Utilize PCIe as underlying bus interface
  Achieve about 1GB/s with one single PCIe 3.0 lane (~ 16GB/s with 16 lanes)
  De facto standard for SSDs, at present time
OS
Communication
SSD

## Slide 7: Background
Block
SSD
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
OS
Communication
SSD
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
A

## Slide 8: Background
SSD
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
OS
Communication
SSD
Block
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
A
B

## Slide 9: Background
SSD
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
OS
Communication
SSD
Block
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
A
B
A

## Slide 10: Background
SSD
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
OS
Communication
SSD
Block
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
X
B
A

## Slide 11: Background
Victim Block
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
SSD
OS
Communication
SSD
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
X
X
A
B
X
X
X
C

## Slide 12: Background
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
SSD
OS
Communication
SSD
Erase
Copy valid pages to new block
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
X
X
A
B
X
X
X
C
A
B
C
Victim Block

## Slide 13: Background
The smallest unit of read/write is page, while reclaim(erase) unit is block
Exploit internal parallelism by grouping erase blocks from each chip into superblock
  Any valid data in victim block will be relocated  write amplification
Internal data movement (via GC) cause long tail latency
  Reducing GC overhead is main goal of SSD research
SSD
OS
Communication
SSD
Host
Interface
Logic
Processor
Buffer Manager
Flash
Controller
Die0
Die1
Die7
Die6
…
Ch0
Ch3
Superblock 0
Superblock 15
Chip
A
B
C

## Slide 14: Abstraction Enhancement
Provide hints to SSD from host
Define hints as optional data entry field that SSD can utilize or ignore
Discard / TRIM
Multi-Stream
Flexible Data Placement
1) Extending Block Abstraction with Host-SSD Hints

## Slide 15: Abstraction Enhancement
Discard / TRIM
  When user delete data, FS mark logical page as invalid  remain in SSD
  Host notice SSD which logical address contains invalid data due to overwrites
  Reduce # of relocated valid pages in GC
  Simple but effective  Most modern OS and storage protocols adopt
1) Extending Block Abstraction with Host-SSD Hints
Filled | Filled | Filled
Filled | Filled | Filled
Filled | Filled | Filled
Free | Free | Free
Filled | Filled | Filled
Filled | Filled | Filled
Filled | Filled | Filled
Free | Free | Free
OS Logical Page Table
SSD Physical Page Table

## Slide 16: Abstraction Enhancement
Discard / TRIM
  When user delete data, FS mark logical page as invalid  remain in SSD
  Host notice SSD which logical address contains invalid data due to overwrites
  Reduce # of relocated valid pages in GC
  Simple but effective  Most modern OS and storage protocols adopt
1) Extending Block Abstraction with Host-SSD Hints
Filled | Filled | Filled
Filled | Filled | Filled
Filled | Deleted | Deleted
Free | Free | Free
Filled | Filled | Filled
Filled | Filled | Filled
Filled | Filled | Filled
Free | Free | Free
OS Logical Page Table
Just mark as tombstone
SSD Physical Page Table

## Slide 17: Abstraction Enhancement
Discard / TRIM
  When user delete data, FS mark logical page as invalid  remain in SSD
  Host notice SSD which logical address contains invalid data due to overwrites
  Reduce # of relocated valid pages in GC
  Simple but effective  Most modern OS and storage protocols adopt
1) Extending Block Abstraction with Host-SSD Hints
Filled | Filled | Filled
Filled | Filled | Filled
Filled | Deleted | Deleted
Free | Free | Free
Filled | Filled | Filled
Filled | Filled | Filled
Filled | Invalid | Invalid
Free | Free | Free
OS Logical Page Table
TRIM
SSD Physical Page Table

## Slide 18: Abstraction Enhancement
Multi-Stream
  Allow hosts to inform SSD physical placement preference of different data
  Similar characteristics may be invalidated at the same time  decrease WAF
  Different stream hints ensure different superblocks
  Supported by Linux kernel since v4.13-rc and NVMe 1.3
  Require manual assignment of stream IDs  need to rewrite application
1) Extending Block Abstraction with Host-SSD Hints
A1
A1
B1
B2
B2
B1
C1
C2
C3
C4
Stream 0 (Hot)
Stream 1 (Warm)
Stream 2 (Cold)
A1
A1
B1
B2
B2
C1
C2
C3
C4
Mixed
Need to copy valid pages (WA!)

## Slide 19: Abstraction Enhancement
Multi-Stream
  AutoStream provide ability to automatically assign stream IDs
  vStream propose virtual streams that different sources can have their own stream
  StoneNeedle and ML-DT apply ML algorithms on assigning stream IDs
  Linux kernel(v5.18-rc1) removed Multi-stream support in bio layer and NVMe driver due to low adoption of vendor
  It is possible to see some schemes built for Multi-stream SSDs appear in ZNS
1) Extending Block Abstraction with Host-SSD Hints

## Slide 20: Abstraction Enhancement
FDP
  Considered an enhanced version of Multi-stream, but more flexible
  Provide ability for hosts configure GC unit based on capability of SSD by providing list of possible FDP configuration
  GC unit granularity can be as small as single erase block or as big as superblock
  Provide statistics and events related to GC to host  learn about SSD internal states
  New NVMe version support FDP formally
1) Extending Block Abstraction with Host-SSD Hints
Namespace
Index | RU Handle ID
0 | 0
1 | 2
2 | 3
RUH0 | RUH1 | RUH2 | RUH3
Reclaim Group
RU0
RU3
RU1
RU2
RU0
RU2
RU3
- RU: Reclaim Unit
- RUH: Reclaim Unit Handle

## Slide 21: Abstraction Enhancement
FDP
  WARCIP provide feedback about GC to host; host dynamically merge and split streams
  PLAN improve performance by dynamically assigning superblocks with different sizes based on write characteristics
1) Extending Block Abstraction with Host-SSD Hints

## Slide 22: Abstraction Enhancement
Host has more control over SSD
Host take over responsibilities of SSD, like metadata management, write buffering and wear-leveling
Not compatible to tr. SSDs  code change required (in app, fs, or driver)
Open-Channel SSD
Zoned Namespaces SSD
2) Enhancing Host Control Over SSD

## Slide 23: Abstraction Enhancement
Open Channel SSD
  Created to provide transparent SSD from host point of view
  Users can directly control placement onto desired channels
  Place too much responsibility on developers
    Applications have to be aware of existence of OC SSD
    Developers have to manage most SSD responsibilities
  Not adopted by industry and replaced by Zoned Namespaces
2) Enhancing Host Control Over SSD

## Slide 24: Abstraction Enhancement
ZNS SSD
  Expose superblocks as zones to host (limited compared to OC-SSD)
  When handling write request, host have to choose zone to write to
  Incoming data have to be sequentially appended to zone
  Host have to manage GC
2) Enhancing Host Control Over SSD
Zone0
Zone1
Zone2
App0
App1
App2
ZNS Controller

## Slide 25: Abstraction Enhancement
ZNS SSD
  ZoneKV, CAZA and WALTZ combine KV store and ZNS SSD
  DFZNSP identify zones mapped to same chips to prevent duplicate writes
  eZNS assign zones into non-conflictable logical zones(v-zone), which can shrink or expand depanding on workload requirement
  Persimmon implement ZNS native by modifying F2FS
2) Enhancing Host Control Over SSD

## Slide 26: Abstraction Enhancement
Reduce latency caused by I/O stack in OS (reducing number and sizes of I/O requests)
Prevent stacking logs on another layer of logs (integrating KV store with SSD)
Computational Storage on SSDs
Key-Value SSD
3) Offloading Host Responsibility to SSD

## Slide 27: Abstraction Enhancement
Computational Storage on SSDs
  SSD allow series of functions(tasklet) to be run on SSD and return result data to host
  Tasklet can only be loaded to SSD internals offline
  No industry standardization effort for tasklet disregarding of storage device
  SmartSSD allow SSD to be programmed for different computational tasks
    Target Hadoop MapReduce type of workload
  YourSQL based on SmartSSD provide early filtering of SQL query results, which reduce # of I/O
  Biscuit enhance ability of SmartSSD with dynamic task loading
  GLIST and GenStore can be used in graph learning and genome sequence analysis in each
3) Offloading Host Responsibility to SSD

## Slide 28: Abstraction Enhancement
Key-Value SSD
  Provide key-value interface instead of block interface
  KAML provide new key-value interface for SSD for removing semantic gaps: between kv-store, VFS and FTL
  PinK improve performance by pinning to levels of LSM-trees
  GPUKV allow direct access between GPU and KV-SSD for reducing I/O overhead
3) Offloading Host Responsibility to SSD
SYSTOR’19 Towards Building a High-Performance, Scale-In Key-Value Storage System
Semantic gap!

## Slide 29: Abstraction Enhancement
Use in CXL
  CPU can directly use SSDs as part of memory system by accessing PCIe-attached SSDs
  Mismatch of granularity can cause traffic amplification (memory: byte, SSD: block)
  2B-SSD allow 2 different access granularities
4) Byte-Addressable SSD
https://ettrends.etri.re.kr/ettrends/206/0905206006

## Slide 30: Future
Storage abstraction should achieve balance of simplicity and configurability

## Slide 31: Conclusion
Traditional storage abstractions have limitations that hinder performance and adaptability for modern storage systems like SSDs.
This survey categorizes and analyzes storage abstraction enhancements into four philosophical approaches, examining their history, relationships, and ecosystem impacts.
By comparing design concepts and implementation, it highlights key insights from industry and academia, addressing partially failed enhancements.
The study identifies future directions for research and development in storage abstraction, aiming to inspire advancements in SSD-focused storage systems.

## Slide 32: Thank you!
2024. 12. 17
Presentation by Yeojin Oh and Nakyeong Kim
oyj5420@dankook.ac.kr nkkim@dankook.ac.kr